## Slide 1
The Chip That Says No
A multi-layer hardware approach to AI safety. Each topic in two slides: the plain version with a picture, then the technical one.
Yobie Benjamin · yobie AT ieee DOT org · linkedin.com/in/yobie
The halt loop: one series current loop through every governor in a rack. Any governor opens it, or a cut wire, and every GPU halts.
Notes: A brief for a short talk. Every topic has two slides: the plain one with a picture for the room, the technical one for the people who will want to argue. Say up front that nothing here is silicon yet: it is a design with a model, tests, hardware blocks and a circuit simulation behind it.

## Slide 2
What this project is
Yobie Benjamin · The Chip That Says No · October 2026
2
A design for a small safety chip that sits beside every AI GPU and holds the only stamp a device needs before it acts. Built in the open as a model with tests, hardware blocks and a circuit simulation. No silicon yet, by choice.
Two open repositories
hardware-and-silicon: the software reference stack and the blog series. safety-governor: the chip design, model, tests, RTL, silicon flow.
One rule for the program
Nothing goes to hardware until the design is proven in software, firmware and circuit simulation: 1000 percent sure in the pre-hardware phase, because tape-out is where mistakes get expensive.
Plan of record: the rack tier
The chip rides on the server maker's management card and reaches NVIDIA's GPU board through its connector. Nothing changes in the GPU or in CUDA.
1 Functional reference
done: every block as software, every attack as a test
2 Formal specification
in progress: invariants written, proofs next
3 Silicon design
written: documents 00 to 18, RTL blocks, loop circuit
4 FPGA emulation
after 3, on a real PCIe or Ethernet path
THE PICTURE
the multi-layer post, roadmap
The same 66 attacks are the acceptance test for every phase, from the software reference to the FPGA. The catalogue is the constant; the artifact changes.
Notes: Set the frame: a design program, not a product. The four phases are the roadmap from the multi-layer post. Phase 1 is done, phase 3 is written, phase 2 is partly done, phase 4 waits. Silicon waits for proof.

## Slide 3
Thesis
Yobie Benjamin · The Chip That Says No · October 2026
3
Safety that lives only in software can be removed by software.
So the decision to act has to be made in silicon the model cannot reach, at the few places where computation turns into effect.
Every layer above the chip is a witness. Only the layer built into silicon can be the lock.
Witness
can keep a gate shut
Safety training
A judge model
A watermark
An observer
A log read later
Lock
is the gate
A ticket the device checks for itself
A switch port that stays shut
A response held at the exit
A breaker that opens
THE PICTURE
the multi-layer post
A judge model is a witness. It can keep a gate shut. It can never be the gate. The layers above the chip are witnesses, and the only layer that can be the lock is the one built into silicon.
Notes: One idea, in the words of the multi-layer post. Witnesses are useful and we keep all of them. But a witness lives in software that the operator, or the model, can change. The lock has to be something that cannot be argued with: a stamp the device checks for itself, a port that does not open, a breaker.

## Slide 4
The thesis, technically: a reference monitor
Yobie Benjamin · The Chip That Says No · October 2026
4
THE THREE TESTS OF A REFERENCE MONITOR: TAMPERPROOF, ALWAYS INVOKED, SMALL ENOUGH TO VERIFY
Property
What it means here
How the governor meets it
Tamperproof
The host, the model and the operator cannot alter the decision logic or the keys
A separate die. Device secret in fuses with no read port. Boot from ROM, extend-only measurement registers, an anti-rollback counter. The rulebook changes only with k-of-n signatures from keys held outside the rack.
Always invoked
There is no path around it
A comparator at every crossing: switch ports open only for roster peers; a device acts only on a ticket; the egress holds a response until a ticket releases it; weights are written only with a ticket; power, reset and clock answer to the governor. Default deny; fail closed.
Verifiable
Small enough that its correctness can be checked
About 2 mm² of core logic as configured (1.4 by 1.4 mm). Invariants written down: no ticket without a rule and its witnesses, no bytes to a stranger, halt on silence, no governor clears its own halt. 200 model tests, 20 RTL tests, an independent audit.
THE FIVE CROSSINGS THE CHIP STANDS AT
bytes leaving the GPU
a request to a device that acts
a response leaving the rack
a write to the weights
GPU power, reset and clock
THE PICTURE
docs 00 and 18
A firewall for actions, with a hand on the breaker: it decides what leaves, and when it must, it also pulls the plug. A chip that can only ask the GPU nicely is a classifier with a heatsink.
Notes: The old idea the design stands on; docs/00 calls verifiability the third test of a reference monitor. Each property has a mechanism, not a promise. The five crossings are the whole attack surface the chip claims to cover; anything that does not pass a crossing is outside the claim.

## Slide 5
The logic behind it
Yobie Benjamin · The Chip That Says No · October 2026
5
The customs officer
She cannot read the language on the paperwork. She does not need to.
the seal
unbroken?
the manifest
matches the count?
the scale
matches the weight?
the list
destination approved?
Smuggling is caught as a mismatch between what the papers say and what the scale says, not by understanding the cargo. The governor works the same way: on structure, never on meaning.
Software safety can be edited out
Refusal lives mostly along one direction in the activation space. Subtract it from the weights and the model answers everything. It takes an afternoon on a consumer GPU.
Watchers can only warn
A judge model is a transformer too: it falls for the same injections, can be edited the same way, and runs as a process the operator can patch or kill.
Hardware checks structure, not meaning
A ticket, a signature from a key the model does not hold, a count under a limit, a peer on a list, a measured workload. A chip can refuse on those.
THE PICTURE
the multi-layer post; docs 17
So: put the decision in silicon, and make the rulebook an allow-list, signed, default deny. No rule, no path. There is no rule for exporting weights.
Notes: Three reasons, one conclusion, and the picture that carries the whole design: the customs officer from docs/17. She checks seal, manifest, weight and the approved list, and catches smuggling as a mismatch. The chip does the same with hashes, signatures, counts and lists. The abliteration and judge facts are from the multi-layer post.

## Slide 6
The logic, technically: what a chip can see
Yobie Benjamin · The Chip That Says No · October 2026
6
Seen at a crossing (small, exact, checkable)
The attested workload: a hash of GPU firmware, host firmware and model weights, measured out of band
The action and its typed fields: strike with a target and a munition; payments.transfer with an amount and a destination
Counts of tokens, cycles and bytes from the GPU's own counters
Whether the peer behind a switch port is on the roster
The rules edition every message was signed under
Signatures: an observer's verdict over a hash, a human's approval over a hold
What the switches actually carried, to cross-check what was presented
Never seen
The meaning of a token. Intent. The chain of thought. Nothing in the rack can look at a stream of integers and say "that is a weapon". A design that promises to catch bad words on the wire promises what no hardware can do.
So meaning is delegated, with three guarantees
To signed lists (protected sites, approved recipients) and to observers (classifiers, people with keys) that sign verdicts over hashes
Always invoked: no verdict, no ticket. Cannot be impersonated: a verdict under the host's key, or the governor's own, is refused. Separate: a different key, a different box, outside the model's reach
THE PICTURE
docs 17, section 1
Two bridges. Tokens and arithmetic bridge the software and the GPU. Hashes, signatures, counters, identities and typed fields bridge the model and the governor. The second bridge is the only one the chip walks on.
Notes: This is the answer to the question asked first: how can a chip know what is bad if it cannot read tokens? It cannot, and it does not try. It checks structure, and it makes the parts that do understand meaning impossible to skip or impersonate. The guarantees are test_observer_is_always_invoked_and_cannot_be_impersonated in H18.

## Slide 7
The proposal: a referee chip beside every GPU
Yobie Benjamin · The Chip That Says No · October 2026
7
The model, on NVIDIA GPUs
Computes freely. Nothing it thinks has any effect until bytes leave or a request is made.
The governor
Checks who is asking, whether a rule allows it, whether the witnesses agree, whether the budget holds. Then signs a ticket, or says no.
The things that act
A weapon, a payment switch, a message gateway, the storage that holds the weights, the rack's own power. Each checks the ticket itself.
request
ticket
Added, not redesigned
It rides on the server maker's management card. Nothing changes in the GPU or in CUDA.
An allow-list, not a blacklist
Signed by a k-of-n quorum whose keys sit outside the chip vendor and the operator. Everything not on it is no.
A hand on the breaker
One series loop through every governor in the rack. Any one opens it, or a cut wire, and every GPU halts.
Buildable now
At the rack tier, with a server maker. The tighter tiers are asks to NVIDIA, firmware and board work, not prerequisites.
THE PICTURE
docs 18, section 1
A referee with a whistle and a rulebook he did not write: the chip holds the whistle, the rulebook is a signed document handed to it. What is burned in is how to enforce; what is loaded is what is allowed.
Notes: The picture to leave in the room: three boxes. The model computes, the governor decides, the devices check the stamp. The four points under it are the design choices that make it buildable: added on existing boards, an allow-list, a physical stop, and a tier that needs no new silicon from NVIDIA.

## Slide 8
Proposal, technically: the module and the die
Yobie Benjamin · The Chip That Says No · October 2026
8
Where it sits and what it reaches
One governor per GPU slot on the OEM's management-module card (DC-SCM class)
Per slot through the HGX connector: SMBus (SMBPBI), power brake, PERST#, PWR_EN, present and fault. HGX reset is grouped today (three PERST inputs for eight GPUs)
NVSwitch port disable out of band through NSM; DPU steering tables through DOCA on the management port
The GPU's confidential-computing attestation taken as an input; the BMC reads through the governor
What is on the die
An OpenTitan-class root of trust: fuses, DICE key chain, OTBN for P-384 signatures (1,697,985 cycles, 17 ms at 100 MHz, so one signature per 50 ms batch), AES-256-CTR with HMAC-SHA-256 for storage
A mailbox of 21 signed commands, checked in order: sequence number, rules edition, signature; the first failure is reported
The policy image and its epoch; the gate core (lookup and comparators); the ledger (budgets, rate windows); a hash-chained log whose head lives in a register
Meter, heartbeat, lever drivers, loop I/O and the signed message fabric between governors
Tier
Where the governor's authority comes from
Status
Rack
Management-card levers, switch and DPU management paths, the halt loop
Plan of record; needs a server OEM, nothing from NVIDIA's silicon
Board
Same firmware, policy format and fabric on a board without a baseboard connector of its own
Fallback; the gaps it leaves are recorded, not hidden
Integrated
Buffer-class checkers in the GPU's copy engines and peer MMU; per-GPU reset
Needs NVIDIA; closes the one gap the rack tier records (H2b)
Notes: The technical shape. Everything in the left column already exists on the boards; the governor is a new user of it. The right column is the die: a root of trust of the OpenTitan kind, plus the gate. The tiers are how the same design degrades or tightens depending on who cooperates. Sources: docs 01, 03, 04, 08 and the board lever register.

## Slide 9
The layers: witnesses above, the lock below
Yobie Benjamin · The Chip That Says No · October 2026
9
5
Governance root
Signs the rulebook, the approved-firmware list and revocations. Separate from the chip vendor on purpose
LOCK
4
Control plane: the gate
Default deny on the only path out: attestation, rulebook, witnesses, budget, human holds, one-time tickets, tamper-evident audit
LOCK
3
Observers
Fast, cheap early-warning verdicts about one request, signed, consumed as witnesses
WITNESS
2
Provenance
Watermark, hardened detector, retrieval, signed registry; emits a signed provenance verdict
WITNESS
1
Model and runtime
The model, CUDA, the serving stack. Treated as untrusted; nothing here is allowed to decide anything
UNTRUSTED
0
Silicon root of trust
Fused device secret, anti-rollback counter, extend-only measurement registers, DICE key derivation, quote engine
LOCK
THE PICTURE
the multi-layer post, layer 3
Biology separates the alarm from the muscle. The spinal reflex pulls the hand off the stove before the brain knows; the early warning is fast, cheap and often wrong, and the system tolerates that because the warning never acts on its own. The layers above the chip are reflexes. The chip is the muscle.
Notes: Six layers, three kinds, straight from the layer table in the multi-layer post. Three are locks: the keys that sign the rulebook, the gate, and the root of trust under it. Two are witnesses the gate can require but never obeys on its own. One, the model, is watched and never trusted. The biology picture is the post's own.

## Slide 10
Layers, technically: mechanism, platform
Yobie Benjamin · The Chip That Says No · October 2026
10
Layer
Mechanism
What it signs or checks
On NVIDIA's platform
5 Governance root
k-of-n quorum over the policy image; rollback refused; expiry enforced
The rulebook (allow-list), the approved-firmware list, revocations
The policy authority's keys; OpenShell's policy prover checks the derived network rules
4 Control plane
Attestation check, rule lookup, witness collection, budget and rate, human hold, one-time ticket bound to a hash of the fields, hash-chained log
Tickets, log checkpoints, the compliance report
OpenShell supervisor middleware today in software; the governor module in hardware; a DOCA application on BlueField-4 next; an I/O-stage block in the GPU eventually
3 Observers
Verdict over the hash of one request: risk, flags, issued and expiry times, under an anchored key
A signed verdict the gate requires on consequential actions
Sentry on BlueField-4 as the required witness; an independent observer as the optional second
2 Provenance
Watermark, hardened detector, retrieval, signed registry
A verdict {registry, content digest, exact | tampered | unknown}
Runs beside the vendor's sampler; its verdict is a witness the gate can require
1 Model and runtime
Measured into the workload hash; routed through the switches and egress the governor controls
Nothing. It can sign nothing the gate accepts
The GPU, CUDA and the serving stack, unchanged
0 Silicon root of trust
Fused device secret, anti-rollback counter, extend-only measurement registers, DICE derivation, quote with a fresh nonce
Quotes: the measurement, the key chain, the counter
The GPU's confidential-computing attestation and the DPU's own root of trust, bound together
Notes: The same six layers with the mechanism named, from the multi-layer post's layer table. The column to watch is the third: what each layer can sign. Only layers 0, 4 and 5 produce something the gate trusts; layer 1 can sign nothing the gate will accept, which is the whole design in one cell.

## Slide 11
How it meets the model
Yobie Benjamin · The Chip That Says No · October 2026
11
1
The model thinks
Token ids in, numbers out. No authority here and none needed.
2
The runtime asks
It turns the output into a typed request: the action and its fields.
3
The governor checks four things
Who is asking. Is there a rule. Do the witnesses agree. Is the budget intact.
4
Ticket, hold, or no
A one-time signed ticket bound to a hash of the exact fields. Or a hold for a human. Or a refusal, logged.
5
The device checks the ticket
Against what it measures itself. A changed amount or target breaks the hash.
6
Act, and record
The action happens and the record goes into a hash chain the chip signs.
THE PICTURE
the multi-layer post, layers 0, 4 and 5
The endpoint that moves the money verifies the ticket itself. Change the amount after the ticket was issued and the hash breaks. Present it twice and the second is refused. The model is never the one who decides.
Notes: Walk the six boxes. The thing to stress is box 5: the device checks the ticket itself, so a lying runtime is caught by the device, not by the governor. The sentence in the strip is the post's own description of the ticket.

## Slide 12
The flow, technically: every check, every refusal
Yobie Benjamin · The Chip That Says No · October 2026
12
Step
What is checked
Fails with (as the model prints it)
Backed by
1
Mailbox
Sequence number, then rules edition, then signature; the first failure is reported
mailbox.bad_sequence, mailbox.bad_signature; a frame from an old edition is refused before the gate sees it
H3: test_mailbox_reports_the_first_failing_check
2
Who is asking
The workload hash (GPU firmware, host firmware, model) and its evaluation attestation
model.not_evaluated
H1 attestation; H18 oversight
3
Is there a rule
Exact rule beats wildcard; typed limits; signed lists for targets and recipients
gate.constraint.target.in_denied_list, endpoint.target_protected
H6 comparator; the strike narration
4
Do the witnesses agree
Observer verdict from a key in the observer set, fresh, under the risk limit; human quorum on holds
gate.witness_missing, gate.held_for_human, release.hazard_class_not_allowed
H17 use cases; H18 oversight; H8 override
5
Is the budget intact
Compute budget and license, session hazard budget, byte budgets, rate windows
release.session_hazard_budget_exceeded, compute.budget_exceeded
H13 shared budget; H18
6
The ticket
Signed over the hash of the exact fields; one use; short expiry; bound to one endpoint
ticket.missing, ticket.replay, ticket.bad_signature, ticket.wrong_endpoint
H17: forged, replayed and wrong-hash tickets never deliver
7
The crossings
Switch ports open only for roster peers; the egress holds responses until released; bytes cross-checked against what was presented
ep.no_capability, gate.output_unpresented
H2 enforcement points; the plot narration
Notes: The same flow with the actual checks and the actual reason codes, as govsim/reasons.py spells them. Every row has a test behind it; the right column names the hypothesis set. If someone wants to see one, python -m govsim.cli usecase strike, hazard, plot or oversight prints the hops.

## Slide 13
Where it stands: drawings tested, no silicon yet
Yobie Benjamin · The Chip That Says No · October 2026
13
200
hypothesis tests pass in the functional model of the governor and a simulated 72-GPU rack (H0 to H18)
20
simulation tests pass on the hard-core RTL blocks, with a LibreLane flow to the open 130 nm process
317 µs
worst case for the halt loop to reach the last of 72 governors, against a 1 ms bound, across 39 simulated configurations
~2 mm²
of core logic for the governor as configured, 1.4 by 1.4 mm, inside a 10 mm² shuttle harness
66
attacks blocked with the predicted reason code in the software reference stack, with all 10 legitimate baselines passing
0
changes needed in the GPU, in CUDA or on the baseboard at the rack tier
THE PICTURE
docs 18, section 3
Everything here is model, RTL simulation and circuit simulation. The two numbers that decide adoption, the real overhead and the false-halt rate, are not measured on hardware yet.
Notes: Honest status. The counts are what pytest prints today: 200 and 20. The loop figure is hw/loop/results.md. The area is docs/04 section 11. The 66 attacks are the reference stack's sweep.

## Slide 14
The challenges, stated plainly
Yobie Benjamin · The Chip That Says No · October 2026
14
The model
no authority needed
The runtime
asks for a ticket
The governor
full authority: signs or refuses
The network
partial: the door, not the conversation
The bank
none, unless it checks the stamp
Reach: the governor's authority ends at the last device that verifies its signature. A payment system is two or three hops away and has never heard of it.
Meaning
The chip guarantees an observer is always invoked. It cannot make the observer right about a disguised request.
False halts
The first support ticket will read: the governor halted my rack. The rate is not measured yet.
The levers
On today's HGX board, reset is grouped and the per-module signals sit in a design guide under NDA.
Cost
One P-384 signature costs 17 ms on the OTBN engine. Batching keeps it under one percent in the model, not yet in silicon.
Governance
Who holds the quorum keys, whose policy governs a shared rack, and the integrated tier needs NVIDIA.
Adoption
A chip wired to nothing that acts is a logger. The first device maker to check a stamp decides this.
THE PICTURE
docs 18, section 5
The perimeter firewall decides whether the packet leaves; it does not decide what the server on the far side does with it. The answer is to move the credential behind a ticket-checking adapter, not to reach through the bank.
Notes: The hop chain is the picture for the deepest challenge, from docs/18 section 5. Authority is full at the governor, partial at the network, and zero at a bank that has never heard of the stamp. The answer, on the next slide, is to move the credential rather than reach through the bank.

## Slide 15
Challenges, technically: mechanism, status
Yobie Benjamin · The Chip That Says No · October 2026
15
Challenge
What the design does
Status
Reach: a payment system two or three hops out
A: the comparator in the device. B: move the credential behind a ticket-checking adapter, so the model's runtime never holds the API key. C: open the DPU flow to the provider only under a live ticket. D: always the signed record
A and C modelled and tested (H6, H2, H17). B is a pattern the endpoint model already expresses; the three-hop payment narration is the next piece of work
Meaning: observers can be fooled
Observer always invoked, cannot be impersonated, separate from the model; hazard classes, legibility floor, session hazard budget, TRNG audit sampling with escrow
Guarantees tested (H17, H18). Observer error rates: open; needs a red team and a quorum of observers on high-hazard classes
False halts
Loop beacon inside the signed heartbeat; loss of current declared after two sense periods (debounce); a jumpered governor caught within two heartbeats; FMEA
Modelled (H11) and simulated (ngspice). Not measured on hardware
Levers on HGX
Per-slot SMBus, power brake, PERST#, PWR_EN at the connector; grouped reset accepted as coarser; the evidence register names what is verified
Evidence register done. Design guide under NDA still needed
Cost
P-384 on OTBN at 1,697,985 cycles (17 ms); one signature per 50 ms window; engine 34 percent busy batched, 272 percent unbatched; firmware share under 0.1 percent of GPU time
Modelled (H9). Silicon or FPGA measurement: open
Governance and adoption
k-of-n quorum with keys outside vendor and operator (goal G8); partitions and per-rule approvers; integrated-tier asks written
Two tenants with two quorums on one baseboard: not designed. Integrated tier: needs NVIDIA
Notes: For each challenge, the mechanism and its status, from docs/18 sections 5 to 8 and the tests named. The status column is the honest part: modelled is not measured, and three of the six end in an ask.

## Slide 16
What I need to prove or disprove the thesis
Yobie Benjamin · The Chip That Says No · October 2026
16
A server maker to talk to
About the management-card slot and the HGX design guide.
A device maker willing to check a ticket
A functional-safety vendor, or whoever runs the tools an agent calls.
A lab with a rack and an FPGA
To measure the real overhead and the false-halt rate over weeks.
A red team
To attack the release gate and the observers with disguised requests.
Chip designers and an auditor
To tear the design apart before any tape-out.
THE PICTURE
the program's own rule
Going to hardware and then tape-out is so expensive that we need to be 1000 percent sure in the pre-hardware phase. These five are what proving, or disproving, the design takes before that. A no is informative.
Notes: Five asks in plain words. Each one maps to a specific open question on the next slide, and several would disprove the thesis as stated if the answer is no.

## Slide 17
What I need, technically: who, what, and why
Yobie Benjamin · The Chip That Says No · October 2026
17
Who
What I need
What it settles
A server OEM
The management-module slot; the HGX design guide under NDA; the connector pinout
Whether per-module levers reach the connector. If not, the rack tier is coarser than the design says
NVIDIA
Seven firmware asks: NSM port-disable semantics, per-GPU reset, buffer-class checkers in the copy engines and peer MMU
The integrated tier; whether the recorded gap (H2b) can be closed from inside the silicon
An endpoint partner
A device or tool gateway that verifies the ticket: P-384 signature, typed fields, epoch, freshness
Whether the comparator works outside the model. If nobody will check the stamp, the thesis fails in practice
A lab with an HGX or NVL rack
An FPGA governor beside a real GPU for weeks
The real overhead against the one percent goal (G6); the false-halt rate; the loop beacon in the field
A model lab's red team
Disguised requests against the release gate and the observers
The size of the semantic residual; whether a quorum of observers is enough
Chip designers, an auditor
Review of the RTL, the firmware plan and the proof-assumption list; formal proofs of the block invariants
Verification before tape-out
What would disprove it
No device that acts will verify a ticket
The levers do not reach the baseboard connector
False halts at a rate operators will not accept
Measured overhead above one percent after batching
Observers miss disguised requests too often for the hazard cases
Nobody will hold the quorum keys
Notes: The asks by who can grant them, from docs/18 sections 8 and 9. The right-hand panel is the falsification list: if any of those six comes true, the design as written does not hold, and we should know early.

## Slide 18
In one sentence
A separate safety chip beside every AI GPU that checks each action the AI attempts against rules signed by people the AI cannot influence, stamps the allowed ones so the devices that carry them out can verify the stamp themselves, and cuts the power when something is wrong.
Yobie Benjamin · yobie AT ieee DOT org · linkedin.com/in/yobie
The AI can think whatever it likes. It cannot act without the stamp, and it cannot forge one.
Added to the server's own boards. Nothing changes in the GPU or in CUDA.
github.com/YobieBenjamin/safety-governor · github.com/YobieBenjamin/hardware-and-silicon
The Chip That Says No, parts 1 to 4, and design documents 00 to 18
Notes: Close on the plain sentence: what it is, what it does, what it can stop. Then the two lines under it. The repositories hold the model, the tests, the RTL, the circuit simulation and the audit; the blog series is the plain-English route in.